CHATTER - Model 308/308D

High cost-effective noise cancelling headsets for call centers. High standard hearing protection to your ears. The newly noise cancellation microphone protects callers from surrounding distraction. Comfortable ear cushions , lightweight headband and flexible cord design, as well as adjustable microphone boom ,work to enhance every-talks good audio quality and all-days wearing comfort.

Description:

Gooseneck microphone boom offers multiple adjustment and accurate talking position

Click-stop headband for different head size and comfortable wearing

Luxurious protein leatherette ear cushion for all-day comfort

Fresh designed T-pad for convenient wearing

Structure features:

Light weight design

Superb receiver audio quality

Excellent noise cancellation

Anti acoustic shock circuit

330°rotatable microphone arm.

180°rotatable joint of speaker and headband

60mm adjustable pliable steel headband

Quick disconnect for leaving desk without taking off headset

Compatible with almost all kinds of phone systems

Technical specifications:

Speaker:

Drive Style: Dynamic (Moving-coiled)

Outer Diameter：φ 27mm

Resistance: 150 Ω+/-20%

Frequency Response: 50HZ-6.8KHZ

Sensitivity: 108±3dB (at 1 KHz 1mw)

MAX Input Power ： 50mW

Distortion: Less 5%

Microphone:

Sensitivity: -44 ±1dB (0dB=1V/Pa, 1 KHz)

Impedance： 2.2K ohm

Directivity: Uni-directional (Noise-cancellation)

Frequency Range : 50HZ ～ 6.8KHZ

Distortion: Less than 3%

Current Consumption:  Max 0.4mA

S/N Ratio: More than 58dB